## Slide 1: Battery Voltage State Indicator Using 741 ANALOG ELECTRONICS 1 ( LAB) Section : C Course Instructor : BISHWAJIT BANIK PATHIK
Group:4
Member:
Name : Id
1. MD.SHARIARE : 16-31825-1
2.ANWAR,NAJMOL : 16-31042-1
3. HASAN, MD. NAHID : 16-31039-1
4. ISLAM, MD. ASIFUL : 16-31081-1
5. HOSSEN, MD. SADDAM : 16-31420-1

## Slide 2
CONTENTS
Introduction
Objective
Circuit Equipment
Project Briefing
Circuit Diagram
Working Methodology
Simulation
Shortcomings
Conclusion

## Slide 3: INTRODUCTION
The 741 IC was designed by Dave Fullagar of Fairchild Semiconductor in 1968
The 741 IC is made ideal for use as integrator, summing amplifier, voltage follower and other basic applications.
Features of 741 IC:
Short circuit and overload protection provided.
Low power consumption.
No latch-up problem.

## Slide 4: OBJECTIVE:
This circuit uses two op-amps in compare mode , which compare the battery with reference voltage.
The circuit shows three state of battery voltage i.e. charged, discharged and normal using three different color LEDs (Red, Green, Yellow).

## Slide 5: Circuit Components
IC
  IC1(741) – 2
Resistor
  R1(2.7K) – 1
  R3(2.7K) – 1
  VR1(22K)
  VR2(22K)
Miscellaneous
  D1,D2( 1N4148) – 2
  LED1-RED
  LED2-ORANGE
  LED3-GREEN

## Slide 6: IC PIN DIAGRAM
OP AMP 741

## Slide 7: Circuit Diagram

## Slide 8: PROJECT FACE:

## Slide 9: WORKING MATHODOLOGY
The battery voltage is connected to E (pin 2 of IC1 and pin 3 of IC2) as show in circuit diagram, which further compares with reference voltage E1 and E2.
If the battery voltage is less then 6V, LED2 glow, similarly if battery voltage is 6V to 9V LED3 glow and if the battery voltage is greater than 9V LED1 glow.
The variable resistors VR1 and VR2 is so adjusted that the voltage between pin 2 of IC1 and earth is 9V and voltage between pin 3 of IC3 and earth is 6V.

## Slide 10: SIMULATION
When voltage is 12V.

## Slide 11: SIMULATION
When voltage is 7V.

## Slide 12: SIMULATION When voltage is 4V.

## Slide 13: SHORTCOMINGS
The major limitations of this project are :
Can not indicated larger amount of voltage.
The variable resistor which set the upper and lower state can change accidently..

## Slide 14: COST ANALYSIS
LIST OF THE PRODUCTS
*BREAD BOARD
*RESISTORS(2.7K,22K)
*JUMPER CABLES
*OP AMP(741)
*BATTERY(9v)
*DIODE
*LED
COSTS
80TK
30TK(200PCS)
65TK
30TK(2PCS)
40TK
15TK(5PCS)
15TK(5PCS)
TOTAL=245TK

## Slide 15: CONCLUSION
Battery voltage state indicator is a small device which we can in our homes to indicate wheather the battery is charged or not.It’s a low cost device which we can build easily.In our homes we use ups,ips,solar panel,all this devices are battery defendant devices Knowing the amount of energy left in a battery compared with the energy it had when it was full gives the user an indication of how much longer a battery will continue to perform before it needs recharging. It is a measure of the short term capability of the battery.So we will be aware of our devices and we can change batteries before the charge runs out and the devices work properly without any barriers.

## Slide 16: QUESTION AND ANSWERS

## Slide 17
THANK YOU